## Slide 1: Quantum Machine Learning
Laurent Boué
Overall survey of the field Live demo: Nearest neighbor classifier on a quantum computer

## Slide 2
Expectation management: Gartner hype cycle for emerging technologies

## Slide 3
From bits to qubits
- Domain-specific quantum annealing
Models of quantum computation:
Outline
- Universal quantum logic gates
Traditional quantum algorithms: a reality check
Quantum chips as AI accelerators
Live demo: nearest neighbor classifier on a quantum computer

## Slide 4
From bits to qubits
General state of qubit: superposition (linear combination basis vectors)
Measurement of a quantum state: “wavefunction collapse”

## Slide 5
From bits to qubits
General state of qubit: superposition (linear combination basis vectors)
Measurement of a quantum state: “wavefunction collapse”
Quantum state defines a probability density function Measurements sample that distribution
Bloch sphere

## Slide 6
Cannot be expressed as
Tensor product between qubits
Not all vectors in tensor product space can be factorized as products!
“Bell state”:
Quantum entanglement
Multiple qubits
Strong correlations between random variables that have no classical analog

## Slide 7
Cannot be expressed as
Tensor product between qubits
Not all vectors in tensor product space can be factorized as products!
“Bell state”:
Quantum entanglement
Quantum computer with n qubits can be in any superposition of 2n states simultaneously
n = 50 qubits  250 complex numbers ~ 18 PB of memory. (PB = 1 million GB)
Multiple qubits
Strong correlations between random variables that have no classical analog
Simulating a quantum system on a classical computer:

## Slide 8
D-Wave systems
Customers include: Lockheed Martin, NASA, Google, Volkswagen, Temporal Defense Systems…
Shielded enclosure interfaced with IO subsystem
Quantum annealing (1/3)
Liquid helium refrigeration
(for comparison interstellar space ~ 2.7K)
First company to have commercial offering Price tag ~ $15m

## Slide 9
Solving optimization problems on rugged energy landscapes
Protein folding Modelling chemical reactions Material discovery Pharmaceutical drug design Satisfiability problems, traveling salesman… Portfolio management Loss functions in machine learning
Quantum annealing (2/3)

## Slide 10
Solving optimization problems on rugged energy landscapes
Protein folding Modelling chemical reactions Material discovery Pharmaceutical drug design Satisfiability problems, traveling salesman… Portfolio management Loss functions in machine learning
Constrained to transverse field Ising model (~ quadratic unconstrained binary optimization QUBO)
Quantum annealing (2/3)

## Slide 11
Quantum annealing overcomes barriers exponentially faster than simulated annealing
Google AI Quantum
~ 2000 qubits but very specific architecture
Quantum annealing (3/3)

## Slide 12
None of these algorithms can be formulated as quantum annealing problems…
Logic quantum gates: designing general (universal) circuits
Traditional quantum algorithms

## Slide 13
”high-level” code
”low-level” circuits
Completely analogous to classic software application
Universal model: any algorithms can be expressed using this quantum gates
In practice, algorithms are usually written at gate-level
(compilers are still very new…)
Logic quantum gates (1/4)

## Slide 14
Unitary matrices: 2x2 for single qubit 4x4 for 2-qubit gate…
Gates can be parametrized by a continuous value: Playground for linear algebra!
Common gates include
NOT gate
CNOT gate
Logic quantum gates (2/4)

## Slide 15
Existing systems: Decoherence time ~ maximum 100 gates
Error correction: no-cloning theorem…
Logic quantum gates (3/4)

## Slide 16
Example circuit: Create entangled state on IBM Q5 (bow-tie architecture)
Sampling superposition state 100 times
Longer circuit would suffer from noisy results…
Logic quantum gates (4/4)

## Slide 17
Traditional quantum algorithms: back to the “usual suspects”

## Slide 18
Shor’s algorithm: Given an integer N, find its prime factors Break public-key cryptography schemes (RSA encryption...)
Multiplication is easy to verify but factorization is much harder
Best classical result ~ exponential in n
Quantum: polynomial in n
exponential speedup
Number of gates ~ 108 for n = 2048…
Traditional quantum algorithms: back to the “usual suspects” (1/3)

## Slide 19
Grover’s search algorithm
Search for subset of items that satisfy a criteria in an unstructured set of N items
Quadratic speedup in the expected number of necessary queries
(basic idea: evaluate search predicate on use superposition of all items in the database)
Traditional quantum algorithms: back to the “usual suspects” (2/3)

## Slide 20
Solving linear systems: HHL algorithm
Given A and b, find x such that:
Traditional quantum algorithms: back to the “usual suspects” (3/3)

## Slide 21
Solving linear systems: HHL algorithm
Exponential speedup in size of matrix NxN
Given A and b, find x such that:
Traditional quantum algorithms: back to the “usual suspects” (3/3)

## Slide 22
Solving linear systems: HHL algorithm
Exponential speedup in size of matrix NxN
Experimental (very complicated) quantum circuit implementing HHL: 2x2 matrix inversion…
“Experimental Quantum Computing to Solve Systems of Linear Equation”, PRL
Given A and b, find x such that:
State preparation (loading data into quantum computer) and gathering read-out statistics (more or less) destroy quantum advantage…
Traditional quantum algorithms: back to the “usual suspects” (3/3)
Unfortunately many constraints: sparse matrices with low condition number, expectation values of projections on x (no access to solution vector itself)…

## Slide 23
“Trendy” idea: use early generation quantum devices as hardware accelerators for machine learning tasks
an emerging interdisciplinary research area
What are quantum computers good for?

## Slide 24
Linear mappings from layer to layer: fused matrix multiplications and accumulate (MACs)
Deep learning in a nutshell: feedforward (memory-less) architectures

## Slide 25
Linear mappings from layer to layer: fused matrix multiplications and accumulate (MACs)
Deep learning in a nutshell: feedforward (memory-less) architectures
Current generation of specialized AI hardware accelerators:
Tensor Core: 4x4 matrix multiply and accumulate / clock cycle Tesla V100 GPU contains 640 Tensor Cores

## Slide 26
Linear mappings from layer to layer: fused matrix multiplications and accumulate (MACs)
Deep learning in a nutshell: feedforward (memory-less) architectures
Quantum gate = multiplication of large matrix
(potentially infinite) with similarly large vector Single operation on quantum computer!

## Slide 27
Bottlenecks: - Data encoding / Read out statistics
- Limited circuit depth (~ flexibility of ML model)
“Circuit-centric quantum classifiers”, arXiv:1804.00633
State preparation with tensor products generates nonlinearities
Quantum chips as AI accelerators

## Slide 28
Use QPU for ”hard to compute” cost function
Gradients provided by rotations on input data
“Classical” updates to the quantum system
Variational circuits: hybrid quantum-classical technique for training!

## Slide 29
Use QPU for ”hard to compute” cost function
Gradients provided by rotations on input data
“Classical” updates to the quantum system
Variational circuits: hybrid quantum-classical technique for training!